Lego crawler by PKW

In this folder there are the 3rd and the 5th version, the 5th one only in the last version folder

This trial start like a copy of the 2011 trial concept trial by miron89, Ive modified it principally 5 times, from the orignal structure to this last version, that probably will join the 2014 model expo Verona, like the 3rd version joined the 2011 one, in the same track of “real” rc trial like axial.

features of the 3rd version:

lenght: 33cm
width: 17cm
minimal height (axes): 4cm
frame height: 6,5cm
maximal height (whitout body): 14cm
speed: 0.25m/s (sariel gear calculator)
weight: 710g
max climbing angle: 35°
max angle between the axes (twist): 60° (approx)
powered by 2rc motors 15.003:1
2 receviers 1 lipo battery pack

value: good speed and torque
lack: power cut-off of the receiver

features of the 5th version:
(the same weihgt and lenght)

widht: 18cm
minimal height (axes): 4cm
frame height: 5,5cm
height (whitout body): 12,5cm
speed: 0.12m/s
max climbing angle: 40°
max angle between the axes (twist): 70° (approx)
powered by 1 XL motor
1 v2 recevier 1 lipo battery box

value: strong structure and lots of power
lack: slow and high body weight