3/8 RCX Output multiplexer

This home-build device controls 8 Fisher-Technik solenoid valves  from 3 ports.

# This is an « easy to build » output multiplexer, for first time in my life I’ve buid an electric circuit. Definitely LEGO is a good way to learn science.

How does it work ?

F-T solenoid valve is an electric to pneumatic controler , as a LEGO pneumatic switch it controls air-flow in pneumatic circuit.

A display on top of the multiplexer allows to control wich of the 8 outputs are activated.

I develop it  to pilot my futur 6 legged pneumatic walker.

| Port A | Port B | Port C | Multiplexer display |
| --- | --- | --- | --- |
| 0 | 0 | 0 | 1 2 | 3 | 5 |  |
| +9v | 0 | 0 | 2 | 3 | 5 |  |
| -9v | 0 | 0 | 1 | 3 | 5 |  |
| 0 | +9v | 0 | 1 2 | 4 | 5 |  |
| 0 | 0 | +9v | 1 2 | 3 | 6 |  |
| 0 | -9v | 0 | 1 2 | 3 | 5 | 7 |
| 0 | 0 | -9v | 1 2 | 3 | 5 | 8 |

## What do you need ?

6 diodes (AN 4002)

6 relays (2 RT,  I used 6V ones but 9V should be better)

8 numeric displays

8 resistors for numeric displays

Resistors depends on how many leds are activated on each numeric display :

1 : 2leds  R1=225 ohm    5 : 5leds R5= 90  ohm

2 : 5leds  R2=  90 ohm    6 : 6leds R6= 75  ohm

3 : 5leds  R3=  90 ohm    7 : 3leds R7=150 ohm

4 : 4leds  R4=112 ohm    8 : 7leds R8= 64  ohm